## Slide 1
GLOBALCODE // CAPSTONE PROJECT
IoT Smart Home
Automation System
Real-Time Appliance Control & Safety Monitoring
Raspberry Pi · Flask · IoT Push Notifications

## Slide 2
Where we're headed
Agenda
01
Problem Statement
02
Solution Overview
03
System Architecture
04
Hardware Components
05
Software & Web Interface
06
Safety System
07
IoT Notifications
08
Live Demo
09
Recommendation & Future Work
10
Q&A
02 / 12
IoT Home Automation

## Slide 3
Why this project exists
The Problem
Traditional homes lack intelligent monitoring and control.
Manual.
Lights, fans, and appliances require physical interaction to operate.
Disconnected.
There's no remote access , you must be home to control anything.
Blind.
Fire and gas leaks go undetected until it's already too late.
Silent.
Homeowners get no instant alert when a hazard occurs while away.
“
How can we make homes smarter, safer, and more responsive using affordable technology?
03 / 12
IoT Home Automation

## Slide 4
What we built
Our Solution
A complete IoT smart-home system built around six core capabilities:
CONTROL
Remote Appliance Control
Toggle lights, fan, and sound system from any device on the network.
FIRE
Flame Detection
IR flame sensor triggers an instant alarm the moment fire is detected.
GAS
Gas Detection
MQ-series gas sensor watches continuously for hazardous leaks.
ALARM
Automatic Alarm
The sound sysconfirmedtem activates on its own the moment danger is.
ALERT
IoT Push Notifications
Real-time alerts land on your phone via ntfy.sh, wherever you are.
UI
Web Dashboard
A responsive, animated control panel reachable from any browser.
04 / 12
IoT Home Automation

## Slide 5
How it all connects
System Architecture
Web Browser — Home Control Dashboard (any device, local network)
↓ HTTP REST API
RASPBERRY PI
Flask Web Server — app.py
Hardware Layer — hardware.py (gpiozero + threading)
↓ GPIO PINS
Room Light
GPIO 17
Hall Light
GPIO 27
Sound System
GPIO 22
Fan (DC Motor)
GPIO 12
Flame Sensor
GPIO 23
Gas Sensor
GPIO 24
↓ ON ALARM
ntfy.sh — Push Notification to Phone
05 / 12
IoT Home Automation

## Slide 6
The physical layer
Hardware Components
Component | Purpose | GPIO Pin
Raspberry Pi | Central processing unit & web server | —
Blue LED | Room Light indicator | GPIO 17
Green LED | Hall Light indicator | GPIO 27
Buzzer / Relay | Sound System (alarm output) | GPIO 22
Yellow LED | Comes on when the alarm triggers | GPIO 12
IR Flame Sensor | Fire detection (digital output) | GPIO 23
MQ Gas Sensor | Gas leak detection (digital output) | GPIO 24
Breadboard & Jumpers | Circuit prototyping | —
Wiring
Outputs (LEDs, motor, buzzer) — Pi GPIO drives the component directly. Inputs (flame, gas) — sensor's digital-out pin feeds back into Pi GPIO. Power — all sensors run from the Pi's 3.3V or 5V rail.
06 / 12
IoT Home Automation

## Slide 7
The code and the dashboard
Software & Web Interface
Layer | Technology | Purpose
Backend | Python 3 + Flask | Web server & REST API
Hardware | gpiozero + RPi.GPIO | GPIO pin management
Frontend | HTML5 + CSS3 + JS | Responsive web dashboard
IoT | ntfy.sh (HTTP POST) | Push notifications
Concurrency | Python threading | Background sensor polling (100ms)
07 / 12
IoT Home Automation

## Slide 8
Flame & gas detection
Safety Detection System
Dual-sensor monitoring: a background thread polls both sensors every 100ms for instant response.
Sensor | Detection Method | Trigger Condition
IR Flame Sensor | RPi.GPIO digital read | GPIO.input(23) == GPIO.LOW
MQ Gas Sensor | gpiozero InputDevice | is_active == True
When an alarm triggers, the system automatically:
01
Sounds the alarm
The sound system (buzzer) activates immediately.
02
Flags the dashboard
A flashing red banner covers the web UI.
03
Notifies your phone
A push alert is sent instantly via ntfy.sh.
04
Names the threat
“FLAME DETECTED” vs “GAS DETECTED” shown clearly.
“
The web alarm shows a red pulsing overlay with a clickable banner — dismissing it also turns off the sound system.
08 / 12
IoT Home Automation

## Slide 9
Alerts on your phone
IoT Push Notifications
Built on ntfy.sh — a free, open-source push service. No app development required; alerts land on Android, iOS, or desktop over plain HTTP.
Sensor
Triggered
→
Python
HTTP POST
→
ntfy.sh
Cloud
→
Phone
Alert
Key Features
URGENT
Urgent priority — bypasses Do Not Disturb on the phone.
TAGGED
Alerts are categorized with fire / warning tags.
UTF-8
Notification body is UTF-8 encoded, so emoji render fine.
TIMEOUT
5-second timeout — a dead network never blocks the system.
09 / 12
IoT Home Automation

## Slide 10
Seeing it work
Live Demonstration
01
Appliance Control
Open the dashboard on a phone or laptop
Toggle Room Light — watch the LED respond
Toggle the Fan — watch the DC motor spin
Toggle the Sound System — hear the buzzer
02
Safety Demo
Trigger the gas sensor
Watch the red alarm banner appear
Show the push notification arriving on the phone
Dismiss the alarm from the web UI
03
Multi-Device Sync
Open the dashboard on two devices at once
Toggle a device from one screen
Watch it update live on the other
10 / 12
IoT Home Automation

## Slide 11
What we learned, what's next
Future Work
Short-term
Camera integration
Temperature / humidity sensors
Data logging
Medium-term
Voice control (Alexa / Google)
Scheduling
Remote internet access
Long-term
Machine-learnign automation
Multi-room support
Energy monitoring
11 / 12
IoT Home Automation

## Slide 12
Thank You
Project Repository
github.com/biileprince/globalcode-homeauto
Technologies Used
Python · Flask · gpiozero · RPi.GPIO · HTML/CSS/JS · ntfy.sh · Raspberry Pi
12 / 12
IoT Home Automation